## Slide 1
JetRover
A Language-Guided Mobile Manipulator
Closing the perception → planning → action → memory loop on real hardware
[ Your Name ] · 2026
Hiwonder JetRover · mecanum base + 5-DOF arm · Orbbec RGB-D camera · ROS
JetRover
1

## Slide 2
Motivation
“I want a coke — can you get me one?”
A useful home / lab robot has to take a vague, natural-language request and carry it out end-to-end — understand it, explore, find the object, and physically fetch it.
[ scene photo: robot in the room ]
JetRover
2

## Slide 3
Why it’s hard
• Long-horizon
“go to A, then B” — chained navigation + manipulation, not one step
• Partially observable
objects and obstacles are unknown until the robot actually sees them
• Real hardware, not simulation
noisy depth, reflective / transparent objects, limited arm reach
• One closed loop
language → navigation → perception → grasp → memory, all tied together
JetRover
3

## Slide 4
The Platform
• Mobile base
4-wheel mecanum — omnidirectional driving
• Arm
5-DOF manipulator + parallel gripper
• Sensing
Orbbec DaBai DCW RGB-D depth camera (eye-in-hand)
• Compute
onboard Jetson, ROS control stack
[ robot photo ]
JetRover
4

## Slide 5
System Architecture
Instruction
Observations
(RGB-D + odometry)
LLM Planner
Subtask Plan
Skill Executor
Navigation
(SLAM + Nav2)
Depth Grasping
(hand-eye + IK)
Controller / ROS 2
Robot + Sensors (Environment)
Perception
(depth → object pose)
Memory: bottles.yaml
plan
obs
re-plan
LLM decomposes the instruction into ordered subtasks and re-plans as new objects are seen
Depth + detection turn raw RGB-D into 3-D object poses
Detections persist to bottles.yaml → long-horizon, resumable tasks
JetRover
5

## Slide 6
Navigation: long-horizon & map-aware
• SLAM + Nav2
Hector SLAM builds the map; Nav2 plans and drives to goals
• Multi-hop goals
“go to A, then B” verified on hardware — two hops, both reached
• Reactive to the world
obstacles that enter the map are planned around
• Tuned for the real bot
throttled teleop + path-bias tuning to stay stable, avoid map corruption
[ rviz map / trajectory screenshot ]
JetRover
6

## Slide 7
Depth-based Grasping
• Pipeline
RGB-D → object detection → hand-eye (eye-in-hand) → IK → approach / descend / close / lift
• First pick on hardware
lifted a wrapped can off the table end-to-end
• Hard problems solved
in-process FK/IK when the vendor IK service returned no solution; nav + grasp share one control node without contending for the serial bus
• Open challenge
reflective / transparent bottles lose depth — robust depth sampling in progress
[ grasp photo / depth view ]
JetRover
7

## Slide 8
Memory closes the loop
• Persist what you see
every detected object is written to bottles.yaml with its pose
• Plan over memory
the LLM filters candidates and orders multi-point navigation to collect them
• Why it matters
this is what turns one-shot reactions into long-horizon, resumable tasks
[ bottles.yaml → planned route diagram ]
JetRover
8

## Slide 9
Experiments — 5-bottle task
Experiment A — targeted collection
Task: fetch all the Coke bottles
Result: 3 / 3 collected
Experiment B — full patrol
Task: visit and log every bottle
Result: 5 / 5 found
Milestone (2026-07-08): first full perception → planning → action → memory loop running on the real robot — LLM candidate filtering + multi-point navigation + on-disk memory.
JetRover
9

## Slide 10
Demo
[ video / GIF ]
Exp A — collect Coke
[ video / GIF ]
Exp B — patrol
JetRover
10

## Slide 11
Key Takeaways
• Full-stack robotics, on real hardware
ROS, Hector SLAM + Nav2, hand-eye calibration, LLM planning + memory, systems debugging
• Hardest wins
nav + grasp coexistence on a single control node; in-process IK; robust depth on tough surfaces
• Honest next steps
reliable grasp on reflective bottles; tighter reach calibration
[ your email ] · [ github / demo link ]
JetRover
11